## Slide 1
Hans Addleman
TransPAC Engineer, International Networks
University Information Technology Services
Indiana University
addlema@iu.edu
INTERNATIONAL
NETWORKS
At Indiana University
Supported by the National Science Foundation
Denial of Service Mitigation
with OpenFlow and SciPass

## Slide 2: Goals
Provide adequate security at 100Gbps speed
Detect Distributed Denial of Service (DDOS) attacks
Stop attack inside the Wide Area Network (WAN)
Automated process
Do not impede legitimate traffic

## Slide 3: Intrusion Detection System
Deep packet inspection
  Look for known traffic patterns and signatures that signal an attack
  Useful for identifying DDOS
Notes: There are many Intrusion detection systems. They allow for deep packet inspection and can trigger on traffic patterns that may signal an attack. The traffic patterns can be manually set or more helpfully look for known signatures. Once the IDS identifies bad traffic it can signal another action. Typically at this point some human intervention may be required to put manual blocks in place.

## Slide 4: SciPass
Indiana University developed SDN Application
  Adaptive IDS cluster load balancing
  Reactive white and blacklisting
  Web Service API for IDS Feedback
  Designed primarily for Science DMZ

## Slide 5: Background: Campus Networks
Campus Networks
  Firewalls
  May not be large flow optimized
  There may be a better path for science / research traffic.

## Slide 6: Background: ScienceDMZ
Support high performance science applications
  Reduce loss that impacts TCP performance
  faster / bigger connection to regional / national / international networks
  Integrate and allow for test points
  Provide some security at 100Gbps
  https://fasterdata.es.net/science-dmz/

## Slide 7: SciPass: Approach
Create a Reactive System
  OpenFlow Switch
  Intrusion Detection
  PerfSonar
Default traffic to slow path
Use IDS to detect what goes on fast path

## Slide 8: SciPass: Default
Traffic follows default path
Traffic mirrored to array of Intrusion Detection Systems.

## Slide 9: SciPass: Detection
IDS identifies science / defined flow
IDS signals SciPass to setup fast path

## Slide 10: SciPass: Bypass
Based on IDS input SciPass installs OpenFlow rules to bypass the firewall / take best path.

## Slide 11: SciPass Blacklist Feature
Can match:
  Source / Destination IP
  Source / Destination Port
  Ethernet Type
SciPass sends OpenFlow rules to switch
  Flow Based: Block HTTP traffic from Host A to B
  Prefix Based: Block all traffic to 192.168.0.1/32
  Prefix Based: Block all traffic to or from 192.168.1.0/24
IDS signals bad traffic to SciPass via web services

## Slide 12: Mitigation
IDS detects malicious traffic
IDS signals SciPass to block traffic
SciPass creates openflow rules on switch to block traffic.

## Slide 13: SciPass Black List Example

## Slide 14: Path Forward
Lab Deployment
  SciPass + Brocade MLXe + IDS (Bro)
  Generate test traffic
  Squash false positives
  Feasibility / Scale
TransPAC4 Field Deployment in logging mode
TransPAC4 Field Deployment in automatic mode

## Slide 15: Questions / Comments?
http://globalnoc.iu.edu/sdn/scipass.html
http://internationalnetworking.iu.edu
Hans Addleman - addlema@iu.edu
TransPAC4 NSF IRNC Award: #1450904